## Slide 1: Modelica Crash Course
Typical mistakes and debugging

## Slide 2: Content
Typical mistakes
Debugging

## Slide 3: Typical mistakes
No pressure boundary
  => Only pressure differences
  => No absolute pressure defined

## Slide 4: Typical mistakes
Division by zero
Model error - division by zero: (0.00023923444976076556*Q_flow) / (m_flow_pipe) = (0.239234) / (0)
Integration terminated before reaching "StopTime" at T = 1

## Slide 5: Typical mistakes
Parameters:
  Unset parameters -> The following parameter doesn't have any value
  Circular dependencies ->
Error: Scalar system is always singular for Q_flow = (0.0)/(0.0) = 0/0
Error: Failed to start model.

## Slide 6: Typical mistakes
Media
  No medium defined
Component type specifier BaseProperties is a partial type.
File: /media/psf/Home/Documents/Software/IDEAS-git/IDEAS/Fluid/Interfaces/ConservationEquation.mo, line 21
Component context: rad.vol.dynBal.medium
Component declared as Medium.BaseProperties medium in Modelica.Media.Interfaces.PartialMedium

## Slide 7: Typical mistakes
Media
  Inconsistent media
The quantity of fan.port_b.m_flow is "MassFlowRate.SimpleLiquidWater" and the quantity of rad.port_a.m_flow is "MassFlowRate.SimpleAir". In connect(fan.port_b, rad.port_a)

## Slide 8: Typical mistakes
Derivative of discontinuous change

## Slide 9: Typical mistakes
Syntax errors
  => Error message from Dymola
  http://modref.xogeny.com
  Code examples in IDEAS
  http://book.xogeny.com

## Slide 10: Typical mistakes
Not connecting ports
  Modelica default: flow variable = 0
Part of the problem for Real elements is overdetermined.
There are 1 scalar equations too many in the set:
fixedHeatFlow.port.Q_flow = 0.0;
fixedHeatFlow.port.Q_flow = 0.0;
which was derived from
fixedHeatFlow.port.Q_flow = -fixedHeatFlow.Q_flow*(1+fixedHeatFlow.alpha*( fixedHeatFlow.port.T-fixedHeatFlow.T_ref));

## Slide 11: Typical mistakes
Not connecting ports
  Modelica default: flow variable = 0
fixedHeatFlow.port.T=29;
It has 2 scalar unknowns and 3 scalar equations

## Slide 12: Typical mistakes
Inconsistent equations
  Parallel branches:

## Slide 13: Content
Typical mistakes
Debugging

## Slide 14: Debugging
Model stage?
  Check -> syntax
  Translation -> mathematical inconsistencies
  Compilation -> related to libraries
  Initialization -> initial equations / initial algorithms
  Simulation -> local mathematical inconsistencies

## Slide 15: Debugging
Tips:
  Read error message!
  Split up model in smaller parts
  Remove model parts
  Use sufficiently high output resolution
  Choose solver accuracy well
  Use simplified boundary conditions
Bug reports:
  https://github.com/open-ideas/IDEAS/issues

## Slide 16: Debugging
Dsmodel files:
  Generates dsmodel.mof file containing ‘flattened’ code