## Slide 1: IDEAS | Buildings
Example
.crash course
13 October 2016
Notes:   10’ - JModelica (demo)
  5’ - Tutorials and reference documentation (slides)
  30’ - Libraries: MSL and own libraries (dymola demo)
  10’ - simman and pymosim (python demo)
  5’ - Coding conventions (slides)
  5’ - Dymola licenses at TME (slides)
1u05 min

## Slide 2
Building
Electric in-home grid
Structure
Occupants
Heating system
Ventilation system
Climate
District heating network
Electric grid
Notes: The first part to model into a building should be the envelope

## Slide 3
IDEAS.Templates.Interfaces.Building
Notes: IDEAS will provide a template, however I do not use it. Just part by part

## Slide 4
IDEAS.Buildings.Components
ZONE
window
slab on ground
outer wall
boundary wall
internal wall
Notes: Types of wall

## Slide 5
IDEAS.Buildings.Data
1
2
3
4
6
5
Construction
Materials
Notes: Create your own walls composition and materials!

## Slide 6: IDEAS | example
Low energy building
Notes:   10’ - JModelica (demo)
  5’ - Tutorials and reference documentation (slides)
  30’ - Libraries: MSL and own libraries (dymola demo)
  10’ - simman and pymosim (python demo)
  5’ - Coding conventions (slides)
  5’ - Dymola licenses at TME (slides)
1u05 min

## Slide 7
Envelope components
Materials
Composition (out→in or propsBus b→a) |  |  |  |  | 
Floor | Tile (d=0.01) | Screed (0.06)* | PUR (0.04) | Concrete (0.20) | Plaster (0.02)
Ceiling | Slate(d=0.01) | PUR(0.18) | Concrete(0,20) |  | 
Exterior wall | Brick (0.10) | MW (0.16) | Brick (0.14) | Plaster (0.02) | 
Interior wall | Plaster (0.02) | Brick (0.10) | Plaster (0.02) |  | 
Slab | Concrete(0.35) | Screed(0.05) |  |  | 
* Floor heating tube is situated at position 2 (between Screed and PUR) |  |  |  |  | 
 | λ (W/mK) | c (J/kgK) | ρ (kg/m3)
Tile | 1.4 | 840 | 2100
Screed | 0.6 | 860 | 1100
Concrete | 1.7 | 840 | 2400
Plaster | 0.6 | 840 | 975
Brick | 1.1 | 840 | 1850
Slate | 2.01 | 760 | 2700
Mineral wool | 0.036 | 840 | 110
PUR | 0.02 | 1470 | 30
Notes:   10’ - JModelica (demo)
  5’ - Tutorials and reference documentation (slides)
  30’ - Libraries: MSL and own libraries (dymola demo)
  10’ - simman and pymosim (python demo)
  5’ - Coding conventions (slides)
  5’ - Dymola licenses at TME (slides)
1u05 min

## Slide 8
Windows
  Glazing: Saint Gobain Clima Plus Futur (U = 1.4 W/m2K, g = 0.755)
  Frame: U-value=2.5 W/m2k , fraction of the window: f=0.15
  Shadowing: On south window
  Window Size: 2m x 1m
Infiltration: n50=0.6 ACH
Ventilation: 36 m3/h per zone, recuperation efficiency 65%
Heating system: ideal heating via radiators or floor heating
Occupancy: 7am-5pm
  Set point: 21oC when occupied, 15 oC otherwise
  Heat gains: 20 W/m2 when occupied, 2 W/m2 otherwise
Notes:   10’ - JModelica (demo)
  5’ - Tutorials and reference documentation (slides)
  30’ - Libraries: MSL and own libraries (dymola demo)
  10’ - simman and pymosim (python demo)
  5’ - Coding conventions (slides)
  5’ - Dymola licenses at TME (slides)
1u05 min