## Slide 1: .crash course
Christina Protopapadaki, Filip Jorissen, Bram van der Heijde & Iago Cupeiro Figueroa
Christina.Protopapadaki@bwk.kuleuven.be Filip.Jorissen@mech.kuleuven.be,
Bram.vanderHeijde@kuleuven.be
Iago.cupeirofigueroa@kuleuven.be
May 3rd, 2017
Notes: This course is for YOU. We can drive the course towards your needs, or what you think it is better for you.

## Slide 2: Modelica crash course
What is Modelica ?
Syntax, language concepts and model structuring
Modelica tools
Use of IDEAS library
Getting started (tutorials, reference docs, libraries, software implementations, ...)
 To get you started with Modelica!

## Slide 3
 | Agenda
11:00 - 11:30 | What is modelica? How does it work?
11:30 - 11:45 | What is Dymola and how does it work? Where to find information?
11:45 – 12:00 | Coffee break & Licence activation (in case)
12:00 – 12:45 | Basic modelica exercise
12:45 - 13:45 | LUNCH BREAK
13:45 - 14:15 | What is IDEAS?
14:15 - 17:30 | IDEAS guided building model

## Slide 4: What is Modelica?

## Slide 5
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden
Notes: Modelica is a language for modeling complex physical systems
Model – a representation of the reality with equations

## Slide 6
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden
Notes: Modelica is a LANGUAGE!!!! – Important
Tools that work using this language – Dymola, Openmodelica...

## Slide 7
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden
Notes: In Modelica Standard Library we can find Mechanical, Electrical, Thermal... components

## Slide 8
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden

## Slide 9
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden
Notes: A-causal modeling: Declarative languages just require the developer to define the problem at a higher level and leaves the solution to the simulation tool
Block-oriented modeling: Procedural programs require the developer to define the order that calculations are to be done in

## Slide 10: What is Modelica
Modelica is a language for modeling of physical systems
  open source
  object oriented
  Acausal modeling (equation based)
  multi-domain
  primarily for simulation, but usable for optimization
  small and large models (> 100 000 equations)
  many model libraries (free and commercial)
  textual and graphical modeling
Notes: A-causal modeling: Declarative languages just require the developer to define the problem at a higher level and leaves the solution to the simulation tool
Block-oriented modeling: Procedural programs require the developer to define the order that calculations are to be done in

## Slide 11: How does Modelica work?

## Slide 12: Equations
Arithmetic operators
  *, /, +, -, ^ (use . for element-wise)
Derivatives
  der(x) = x ~
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden
Notes: Modelica is a programming language. Overview of the most important parts of the syntax

## Slide 13: Logical operators, control flow
Logical
  and, or, not
Conditional
  If, elseif, else
Loops
  For
Comparing numbers
  >, <, <>, >=,…

## Slide 14: Models
From M. Tiller, Modelica by Example, http://book.xogeny.com
# variables = # equations!
Balanced
Close line with ;
Notes: A lot of types defined in the Modelica standard library Modelica.SIunits.Type

## Slide 15: Comments
Very important!
Comments regarding components, parameters, variables
  “this is a comment”
  Can show up in graphical interface
Line comments
  // This is a comment on one line
  /* This is a comment over multiple lines */

## Slide 16
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden
Notes: We cannot connect, for example, an electrical line with a heat flow

## Slide 17: Connectors
Usually
  Signal in out
  Fluid flow (mass flow rate, pressure, enthalpy)
  Heat flow (heat flow rate, temperature)
flow variable, potential variable
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden
Notes: Electrical: flow variable is current, potential variable is voltage
Mechanical: flow variable is force, potential variable is position
Thermal: flow variable is heat flow, potential variable is temperature
Connect two components is equal as applying Kirchoff equations

## Slide 18: Components
Instances of a model
model name usually Capitalized, instance not
  Wall innerWall(res = 200, A = 10);
public variables and parameters can be accessed with dot notation, e.g.:
  heatPort.Qflow
  wall.res
Protected variables/params cannot be accessed
  Don’t show up in simulation results
Notes: When we have a model defined, we can drag that model as a subcomponent to other model as an instance
When defining variables and parameters, you can state a protected paragraph

## Slide 19: Inheritance
Model inherits from other model
  Variables, parameters, equations
extends keyword
partial model
Code can be managed more easily
Example
Notes: With partial model we define a model that is not completed, thus when extending it will need some extra information

## Slide 20
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden
Notes: For CelestialBody we will need equations for mass, name and radius
For Rocket we will need 3 more equations: name, thrust and gravity

## Slide 21
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden
Notes: In moond landing we define the remaining parameters: both names, and thrust and gravity for Rocket
Notice the dot notation

## Slide 22: Inheritance and connectors
Slides from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden
Notes: Another example of inheritance

## Slide 23
Slide from Peter Fritzson, Introduction to Object-Oriented Modeling, Simulation and Control with Modelica, Tutorial for Modelica Conference 2011, Dresden
Notes: Good code management

## Slide 24: Records
Data records can be created to collect parameter information regarding a model
Pros
  Keep data separate from models
  Easy model parametrization with drop-down list
  Easy to see what data is used in a particular model
Notes: This records can be instantiated in the model so that you can refer them afterwards with the dot notation

## Slide 25: Functions
Modelica also allows the creation of functions
Calling the function
It is possible to have several outputs
Notes: It is also possible to create your own functions for later code use
Define inputs and outputs

## Slide 26: Blocks
For causal formalisms
Used in control systems
Picture from http://book.xogeny.com/components/components/block_comps/
Notes: Modelica also have a series of blocks for causal modelling, used in the control systems

## Slide 27: How does Dymola work?

## Slide 28: Modelica environments
Commercial software tools
Dymola (Dassault Systèmes, Sweden)
MathModelica (MathCore, Sweden)
SimulationX (ITI, Germany)
MapleSim (Maplesoft, Canada)
Free and open source tools
OpenModelica (Open Source Modelica Consortium, Sweden and other countries)
JModelica (Modelon, Sweden)

## Slide 29: What does Dymola do?
Compiles and integrates equations
  Finds solution to ODEs at indicated times
  
  Different solvers
    Radau, Dassl, Euler, Runge-Kutta,…
    Define start and end time, time step
    Define Solver tolerance
Simulates model
Plots output
Notes: No optimization

## Slide 30: Graphical user interface

## Slide 31: Packages
Packages are a way to organize models in a structured way
  Hierarchical structure
  Any number of levels can be defined
  A way to group models of similar type in one place
  Easy to find a particular model

## Slide 32: Graphical user interface
Notes: Use check constantly

## Slide 33: Graphical user interface

## Slide 34: Graphical user interface

## Slide 35: Graphical user interface
Command Shell
Variable Browser
Main Menu Bar
Task Bar
Plot Diagrams

## Slide 36: Exporting results
All results in the Variable Browser can be exported
To export a result, right-click the name of the result and select Save As…
There are several formats to which the result can be saved
  .mat (Matlab format can also be opened in Dymola)
  .csv (for use in e.g. Excel)
  .txt

## Slide 37: Interface with other programs
Scripting
  Parameter variation
  Parallel simulations
  Optimal control
Python scripts using BuildingsPy
  Nice for plotting
  http://simulationresearch.lbl.gov/modelica/buildingspy/
MATLAB
  Built-in with Dymola

## Slide 38: Websites
General
www.modelica.org
www.openmodelica.org
www.jmodelica.org
http://www.claytex.com/tech-blog/
Modelica language
http://modref.xogeny.com/ !!!
http://book.xogeny.com/ !!!
KUL modeling conventions
https://docs.google.com/document/d/1MaNKTdLz-YPpEEH3Eg12ECzG0ErK-rIK9IHd6gsBp7Q/edit?usp=sharing
Libraries:
https://github.com/open-ideas --> IDEAS + Crash Course
https://simulationresearch.lbl.gov/modelica --> look at Buildings.Examples.Tutorial
Annex 60: https://github.com/iea-annex60/modelica-annex60
Dymola user guide
Volume 1 & 2: C:\Program Files (x86)\Dymola 2017\Documentation\Dymola User Manual Volume 1 or via Dymola > help.

## Slide 39: Fora
http://www.openmodelica.org/index.php/forum
http://www.jmodelica.org/forum
www.stackoverflow.com (tag Modelica)
And last but not least: https://groups.google.com/d/forum/modelicans

## Slide 40: Use of Dymola with KULeuven license
Access to a floating licence (on the building physics server).
Connected physically (cable) to the building physics or mech network
Open Dymola and go to help>licence..
Enter 10.112.72.4 and follow instructions
More information on Modelicans (google groups)

## Slide 41: Break
Time to activate and borrow your license!